## Slide 1
Chapter 6
Performance Considerations

## Slide 2
Performance Optimizations
Performance optimizations covered so far:
  Tuning resource usage to maximize occupancy
    Threads per block, shared memory per block, registers per thread
  Minimizing control divergence to increase SIMD efficiency
  Shared memory tiling to increase data reuse
More optimizations covered today:
  Memory coalescing
  Thread coarsening

## Slide 3
DRAM Cell
Enable
In/Out
A DRAM cell consists of a capacitance that stores a charge and a three-state device (single transistor) that allows data to be read/written (capacitor discharge/charged)

## Slide 4
DRAM Array
…
…
…
…
A DRAM bank consists of a 2D array of DRAM cells activated one row at a time, and read at the column
activate row
read one bit from each column

## Slide 5
DRAM Bank
DRAM Array
Row Decoder
Sense Amps
Column Latches
Mux
Row Address
Column Address
Data
Burst
Slow
Relatively Faster

## Slide 6
DRAM Bank Example
0 | 1 | 0
Address

## Slide 7
DRAM Bank Example
0 | 1 | 0
Row Decoder
Address
Use part of the address to select the row

## Slide 8
DRAM Bank Example
0 | 1 | 0
Row Decoder
Address
Mux
Read the entire row (burst)

## Slide 9
DRAM Bank Example
0 | 1 | 0
Row Decoder
Address
Mux
Use other part of the address to select columns within row

## Slide 10
DRAM Bank Example
0 | 1 | 1
Row Decoder
Address
Mux
If other access from the same burst, no need to read the row again

## Slide 11
DRAM Burst
Accessing data in different bursts
  Need to access the array again
Accessing data in the same burst
  No need to access the array again, just the multiplexer
Accessing data in the same burst is faster than accessing data in different bursts
Timeline:
Timeline:

## Slide 12
Memory Coalescing
When threads in the same warp access consecutive memory locations in the same burst, the accesses can be combined and served by one burst
  One DRAM transaction is needed
  Known as memory coalescing
If threads in the same warp access locations not in the same burst, accesses cannot be combined
  Multiple transactions are needed
  Takes longer to service data to the warp
  Sometimes called memory divergence

## Slide 13
Memory Coalescing Examples
Vector addition:
  Accesses to x, y, and z are coalesced
    e.g., threads 0 to 31 access elements 0 to 31, resulting in one memory transaction to service warp 0
Matrix-matrix multiplication:
  Accesses to A and B are coalesced
    e.g., threads 0 to 31 access element 0 of A on the first iteration, resulting in one memory transaction to service warp 0
    e.g., threads 0 to 31 access elements 0 to 31 of B on the first iteration, resulting in one memory transaction to service warp 0
int i = blockDim.x*blockIdx.x + threadIdx.x;
z[i] = x[i] + y[i];
int row = blockDim.y*blockIdx.y + threadIdx.y;
int col = blockDim.x*blockIdx.x + threadIdx.x;
for(unsigned int i = 0; i < N; ++i) {
sum += A[row*N + i]*B[i*N + col];
}
Note: a warp contains consecutive threads in the x dimension followed by the y dimension

## Slide 14
Memory Coalescing Examples
Tiled matrix-matrix multiplication:
  Accesses to A and B are coalesced
    e.g., threads 0 to 31 access elements 0 to 31 of A on the first iteration, resulting in one memory transaction to service warp 0
      Even better than without tiling where all threads accessed one element, underutilizing the burst
    e.g., threads 0 to 31 access elements 0 to 31 of B on the first iteration, resulting in one memory transaction to service warp 0
unsigned int row = blockIdx.y*blockDim.y + threadIdx.y;
unsigned int col = blockIdx.x*blockDim.x + threadIdx.x;
for(unsigned int tile = 0; tile < N/TILE_DIM; ++tile) {
A_s[threadIdx.y][threadIdx.x] =
A[row*N + tile*TILE_DIM + threadIdx.x];
B_s[threadIdx.y][threadIdx.x] =
B[(tile*TILE_DIM + threadIdx.y)*N + col];
...
}

## Slide 15
Multiple DRAM Banks
DRAM Array
Row Decoder
Sense Amps
Column Latches
Mux
DRAM Array
Row Decoder
Sense Amps
Column Latches
Mux
DRAM Array
Row Decoder
Sense Amps
Column Latches
Mux

## Slide 16
Latency Hiding with Multiple Banks
With one bank, time still wasted in between bursts
Latency can be hidden by having multiple banks
Need many threads to simultaneously access memory to keep all banks busy
  Achieved with having high occupancy in SMs
    Similar idea to hiding pipeline latency in the core

## Slide 17
Fine-Grain Thread Granularity
So far, parallelization approaches made threads as fine-grain as possible
  Assign smallest possible unit of parallelism per thread
    e.g., one vector element per thread in vector addition
    e.g., one output pixel per thread in RGB to gray and in blur
    e.g., one output matrix element per thread in matrix-matrix multiplication
Advantage: provide hardware with as many threads as possible to fully utilize resources
  If more threads provided than GPU can support, hardware can serialize the work with low overhead
  If future GPUs come out with more resources, they can extract more parallelism without code being rewritten
    Recall: transparent scalability
Disadvantage: if there is a “price” for parallelizing work across more threads, this price is maximized
  Okay if threads actually run in parallel
  Suboptimal if threads are getting serialized by hardware

## Slide 18
Recall: Vector Addition
Input Vector x:
Input Vector y:
Output Vector z:
What price was paid to parallelize work across more threads?
None. Making threads as fine-grain as possible is a good approach.

## Slide 19
N
N
N
Recall: Tiled Matrix-Matrix Multiplication
C = A x B
A
B
C
N
N
N
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
What price was paid to parallelize work across more threads?

## Slide 20
N
N
N
Recall: Tiled Matrix-Matrix Multiplication
C = A x B
A
B
C
N
N
N
What price was paid to parallelize work across more threads?
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝ | ⇝
Thread blocks processing horizontally adjacent output tiles of C redundantly load the same input tile of A

## Slide 21
N
N
N
Optimizing Tiled Matrix-Matrix Multiplication
C = A x B
A
B
C
N
N
N
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
 |  |  |  |  |  |  |  | ⇝ | ⇝ | ⇝ | ⇝ |  |  |  | 
Optimization: Have one thread block process multiple output tiles sequentially and reuse the input tile that it loaded

## Slide 22
Example: Tiled Matrix-Matrix Multiplication
__global__ void mm_tiled_coarse_kernel(float* A, float* B, float* C, unsigned int M,
unsigned int N, unsigned int K) {
__shared__ float A_s[TILE_DIM][TILE_DIM];
__shared__ float B_s[TILE_DIM][TILE_DIM];
unsigned int row = blockIdx.y*blockDim.y + threadIdx.y;
unsigned int colStart = blockIdx.x*blockDim.x*COARSE_FACTOR + threadIdx.x;
float sum[COARSE_FACTOR];
for(unsigned int c = 0; c < COARSE_FACTOR; ++c) {
sum[c] = 0.0f;
}
for(unsigned int tile = 0; tile < N/TILE_DIM; ++tile) {
// Load A tile
A_s[threadIdx.y][threadIdx.x] = A[row*N + tile*TILE_DIM + threadIdx.x];
for(unsigned int c = 0; c < COARSE_FACTOR; ++c) {
unsigned int col = colStart + c*TILE_DIM;
// Load B tile
B_s[threadIdx.y][threadIdx.x] = B[(tile*TILE_DIM + threadIdx.y)*N + col];
__syncthreads();
// Compute with tile
for(unsigned int i = 0; i < TILE_DIM; ++i) {
sum[c] += A_s[threadIdx.y][i]*B_s[i][threadIdx.x];
}
__syncthreads();
}
}
for(unsigned int c = 0; c < COARSE_FACTOR; ++c) {
unsigned int col = colStart + c*TILE_DIM;
C[row*N + col] = sum[c];
}
}
Thread responsible for multiple output elements
Processing for each output element is serialized with a coarsening loop
dim3 numBlocks((N + TILE_DIM - 1)/TILE_DIM/COARSE_FACTOR, (N + TILE_DIM - 1)/TILE_DIM);

## Slide 23
Thread Coarsening
Thread coarsening is an optimization were a thread is assigned multiple units of parallelism to process
  i.e., a thread is made more coarse-grain
Advantages:
  Reduces the “price” paid for parallelization
    Redundant memory loads in the tiled matrix multiplication
    Could be redundant computations in other examples
    Could be synchronization overhead or divergence (covered later)
Disadvantages:
  Underutilizes resources if coarsening factor is too high
    Need to retune coarsening factor for each device
  More resources per thread which may limit occupancy

## Slide 24
Checklist of Common Optimizations
Optimization | Benefit to Compute Cores | Benefit to Memory | Strategies
Maximizing occupancy | More work to hide pipeline latency | More parallel memory accesses to hide DRAM latency | Tuning usage of SM resources such as threads per block, shared memory per block, and registers per thread

## Slide 25
Checklist of Common Optimizations
Optimization | Benefit to Compute Cores | Benefit to Memory | Strategies
Maximizing occupancy | More work to hide pipeline latency | More parallel memory accesses to hide DRAM latency | Tuning usage of SM resources such as threads per block, shared memory per block, and registers per thread
Enabling coalesced global memory accesses | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic and better utilization of bursts/cache-lines | Transfer between global memory and shared memory in a coalesced manner and performing un-coalesced accesses in shared memory (e.g., corner turning) Rearranging the mapping of threads to data Rearranging the layout of the data

## Slide 26
Checklist of Common Optimizations
Optimization | Benefit to Compute Cores | Benefit to Memory | Strategies
Maximizing occupancy | More work to hide pipeline latency | More parallel memory accesses to hide DRAM latency | Tuning usage of SM resources such as threads per block, shared memory per block, and registers per thread
Enabling coalesced global memory accesses | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic and better utilization of bursts/cache-lines | Transfer between global memory and shared memory in a coalesced manner and performing un-coalesced accesses in shared memory (e.g., corner turning) Rearranging the mapping of threads to data Rearranging the layout of the data
Minimizing control divergence | High SIMD efficiency (minimizing idle cores during SIMD execution) | - | Rearranging the mapping of threads to work and/or data Rearranging the layout of the data

## Slide 27
Checklist of Common Optimizations
Optimization | Benefit to Compute Cores | Benefit to Memory | Strategies
Maximizing occupancy | More work to hide pipeline latency | More parallel memory accesses to hide DRAM latency | Tuning usage of SM resources such as threads per block, shared memory per block, and registers per thread
Enabling coalesced global memory accesses | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic and better utilization of bursts/cache-lines | Transfer between global memory and shared memory in a coalesced manner and performing un-coalesced accesses in shared memory (e.g., corner turning) Rearranging the mapping of threads to data Rearranging the layout of the data
Minimizing control divergence | High SIMD efficiency (minimizing idle cores during SIMD execution) | - | Rearranging the mapping of threads to work and/or data Rearranging the layout of the data
Tiling of reused data | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic | Placing data that is reused within a block in shared memory or registers so that it is transferred between global memory and the SM only once

## Slide 28
Checklist of Common Optimizations
Optimization | Benefit to Compute Cores | Benefit to Memory | Strategies
Maximizing occupancy | More work to hide pipeline latency | More parallel memory accesses to hide DRAM latency | Tuning usage of SM resources such as threads per block, shared memory per block, and registers per thread
Enabling coalesced global memory accesses | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic and better utilization of bursts/cache-lines | Transfer between global memory and shared memory in a coalesced manner and performing un-coalesced accesses in shared memory (e.g., corner turning) Rearranging the mapping of threads to data Rearranging the layout of the data
Minimizing control divergence | High SIMD efficiency (minimizing idle cores during SIMD execution) | - | Rearranging the mapping of threads to work and/or data Rearranging the layout of the data
Tiling of reused data | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic | Placing data that is reused within a block in shared memory or registers so that it is transferred between global memory and the SM only once
Privatization (covered later) | Fewer pipeline stalls waiting for atomic updates | Less contention and serialization of atomic updates | Applying partial updates to a private copy of the data then updating the universal copy when done

## Slide 29
Checklist of Common Optimizations
Optimization | Benefit to Compute Cores | Benefit to Memory | Strategies
Maximizing occupancy | More work to hide pipeline latency | More parallel memory accesses to hide DRAM latency | Tuning usage of SM resources such as threads per block, shared memory per block, and registers per thread
Enabling coalesced global memory accesses | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic and better utilization of bursts/cache-lines | Transfer between global memory and shared memory in a coalesced manner and performing un-coalesced accesses in shared memory (e.g., corner turning) Rearranging the mapping of threads to data Rearranging the layout of the data
Minimizing control divergence | High SIMD efficiency (minimizing idle cores during SIMD execution) | - | Rearranging the mapping of threads to work and/or data Rearranging the layout of the data
Tiling of reused data | Fewer pipeline stalls waiting for global memory accesses | Less global memory traffic | Placing data that is reused within a block in shared memory or registers so that it is transferred between global memory and the SM only once
Privatization (covered later) | Fewer pipeline stalls waiting for atomic updates | Less contention and serialization of atomic updates | Applying partial updates to a private copy of the data then updating the universal copy when done
Thread coarsening | Less redundant work, divergence, or synchronization | Less redundant global memory traffic | Assigning multiple units of parallelism to each thread in order to reduce the “price of parallelism” when it is incurred unnecessarily

## Slide 30
Tensions Between Optimizations
Maximizing occupancy
  Maximizing occupancy hides pipeline latency, but too many threads may compete for the cache, evicting each others’ data (thrashing the cache)
Shared memory tiling
  Using more shared memory enables more data reuse, but may limit occupancy
Thread coarsening
  Coarsening reduces parallelization overhead, but requires more resources per thread which may limit occupancy
Need to find the sweet spot that achieves the best compromise

## Slide 31
Know Your Application’s Bottleneck!
The constraint that limits the performance of an application on a device is called a bottleneck
The bottleneck depends on the application as well as the device itself
Optimizations trade one resource for another to alleviate the bottleneck
Make sure to properly diagnose your application’s bottleneck before applying optimizations
  Otherwise, you may be optimizing for the wrong resource

## Slide 32
References
Wen-mei W. Hwu, David B. Kirk, and Izzat El Hajj. Programming Massively Parallel Processors: A Hands-on Approach. Morgan Kaufmann, 2022.